## Slide 1: Intermediate CPU and Data Flow

## Slide 2: Group members:
Talha Zeeshan
Muhammad Bilal
Sarmad Saeed
Ahmad Nawaz

## Slide 3: Intermediate CPU and Data Flow:
Key Components in CPU Data Flow
Registers:
  Small, fast storage units inside the CPU (like R0, R1, Accumulator, etc.).
  Data moves between registers during calculations.
ALU (Arithmetic Logic Unit):
  Executes math operations (+, -, *, /) and logic operations (AND, OR, NOT, etc.).
Control Unit:
  Directs traffic inside the CPU — tells the ALU, registers, and memory what to do.
Buses:
  Data Bus: moves actual data (like numbers).
  Address Bus: moves memory addresses.
  Control Bus: moves control signals (read/write commands).
Cache:
  Super-fast memory inside the CPU to store frequently used data.
  Reduces time needed to fetch data from the slower main memory.

## Slide 4: CPU Data Flow (Intermediate Level)
Fetch:
  The CPU fetches an instruction from memory (RAM) using the Program Counter (PC), which points to the address of the next instruction.
  The instruction gets loaded into the Instruction Register (IR).
Decode:
  The Control Unit (CU) decodes the instruction to figure out what operation needs to happen.
  It sets up signals that control other parts of the CPU.
Execute:
  The instruction is carried out.
  This could mean performing an ALU operation (Arithmetic Logic Unit, like addition), moving data, or changing the PC (like jumping to a new instruction).
Memory Access (sometimes):
  If the instruction involves reading from or writing to memory, the Memory Management Unit (MMU) and cache system help transfer data efficiently.
Write Back:
  The result (say from an ALU calculation) gets written back to a register or memory.

## Slide 5: Memory address translation:
Memory address translation is the process of mapping:
a virtual address (used by a program to access memory.)→ to a physical address(real location
in RAM)
so the CPU can access data correctly.

## Slide 6
Step | Action | Description | Example
1 | Program uses Virtual Address | Program asks for data using a virtual address. | A program wants to get data from virtual address 0x10.
2 | CPU sends Virtual Address to MMU | CPU sends the virtual address to the Memory Management Unit (MMU) to translate it. | CPU sends 0x10 to the MMU.
3 | MMU splits Address | The MMU splits the virtual address into a Page Number and Offset. | 0x10 → Page Number = 1, Offset = 16. (Page size = 32 bytes)
4 | MMU checks Page Table | The MMU checks the Page Table to see where the virtual page is stored in physical memory. | Page Table says: Virtual Page 1 → Physical Frame 3.
5 | MMU calculates Physical Address | MMU calculates the exact physical address using the frame number and offset. | (3 × 32) + 16 = 112 (physical address).
6 | CPU accesses Physical Memory (RAM) | CPU reads or writes the data at the physical address. | CPU reads data from RAM at address 112.
How it Works (with Example)

## Slide 7: Register Transfer Language (RTL):
RTL describes how data moves (transfers) between registers and what operations happen to that data inside a CPU, at a very low level.
Key Concepts in RTL
Registers: Small storage inside CPU (R1, R2, MAR, PC, etc.)
Micro-operations: Tiny operations like moving data, adding numbers, incrementing counters.
Control Signals: Tell the hardware when to do a transfer or operation.

## Slide 8: Common Special Registers:
PC: Program Counter (points to next instruction)
IR: Instruction Register (holds current instruction)
MAR: Memory Address Register (holds address for memory access)
MDR: Memory Data Register (holds data read/written from/to memory)
ACC: Accumulator (used for intermediate ALU results)

## Slide 9
RTL Notation | Meaning
R3 ← R1 + R2 | Add R1 and R2, store result in R3
PC ← PC + 1 | Increment the Program Counter (next instruction)
MDR ← Memory[MAR] | Load data from memory address MAR into MDR
Memory[MAR] ← MDR | Store data from MDR into memory at address MAR

## Slide 10: What are Data Hazards?
In pipelined processors, a data hazard occurs when an instruction depends on the result of a previous instruction that has not yet completed its path through the pipeline.It leads to incorrect or delayed data being used.
There are 3 main types:
1. RAW (Read After Write):Instruction needs a value that hasn't been written yet. (Most common)
2. WAR (Write After Read):A later instruction writes before an earlier one reads.
3. WAW (Write After Write):Two instructions write to the same destination in the wrong order.

## Slide 11: Solutions for Data Hazards
Forwarding(Data Bypassing)
Concept:
Instead of waiting for a result to be written back to the register file, we forward (pass) the result directly from one pipeline stage to another.
Example:
If Instruction 1 produces a result in the EX stage, and Instruction 2 needs it in the next EX stage — we pass it directly from Instruction 1’s EX stage to Instruction 2’s EX stage.

## Slide 12: Advantage:
Reduces stalls
Speeds up pipeline
Diagrammatically:
Instruction 1:
EX → MEM → WB
Instruction 2:
EX (gets result from Instruction 1's EX stage)
2. Stalling (Pipeline Stall / Bubble):
If forwarding isn't possible (for example, if the data isn't yet available), the processor pauses the pipeline for a cycle or two (inserts a 'bubble') until data is ready.
How it works:
Control logic detects the hazard
Inserts a NOP (No Operation) instruction
Resumes execution when data is ready.

## Slide 13: Disadvantage:
Slows down the pipeline (wastes cycles)
Quick Example:
ADD R1, R2, R3 // R1 = R2 + R3
SUB R4, R1, R5 // Needs R1 immediately
Without Forwarding → stall
With Forwarding → pass result directly from ADD to SUB

## Slide 14: THANKS